10525 Willows Road NE

Redmond, WA 98052

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

Fax: 425.867.6972

pmhelp@data-io.com

SUBJECT: PP100 Remove Coaxial cable & Install UTP cable

| MODELS AFFECTED | 2500 |  | 3000 |  | 7000 |  | 7500 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | PP100 | X | 9500 |  | 970 |  | T/R |  | ALL |  |

- Purpose: To remove Coaxial cable between Handler Computer and PC104 Rack and install a UTP cable between Handler Computer and Network Hub within the PP100.

- Tools required: None

- Equipment Required:

UTP Cable, Data I/O P/N: 411-0017-001 “Cable,Pair,Twisted”

- Instructions:-

- Exit from all programs and shut down the the Handler Computer and turn off the power from the front rotary switch.

- Remove the T-connector, 50-Ohm Terminator and the coaxial cable from the BNC connector on the Network Interface Card (NIC) installed on the Handler Computer.

- Remove the coaxial cable’s other end which is attached to the BNC connector on the lower PC104 rack.

- Install the 50-Ohm terminator, removed in step-1, to the now empty BNC connector on the lower PC104 rack.

- Install the Unshielded Twisted Pair (UTP) cable (P/N 411-0017-001) to one of the empty RJ-45 sockets on the 3COM® 4-port HUB.

- Install the other end of the UTP cable to the RJ-45 socket on the NIC of Handler Computer.

- Test:-

Power up the PP100, start AH400 and ensure that all PC104 computers connect to the Network.