#### DATA I/O Corporation

# 10525 Willows Road NE

Redmond, WA 98052

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

FAX: 425.867.6972

pmhelp@dataio.com

### Subject: PP100 Vacuum Switch Adjustment

Model Affected: PP100

1.0	PURPOSE: To inform customers how to adjust the vacuum switch on the PP100.

2.0	TOOLS REQUIRED:  Small Flat blade screwdriver.

3.0	PARTS REQUIRED: NONE

- INSTRUCTIONS:  The PP100 has 1-3 vacuum switches depending of if you have an option bay or not.  The vacuum switches are located as follows.  1 switch is on the SMAC head and 1 on each cup of the option bay shuttle system.  These vacuum switches are all the same model.

  - The reason to adjust the vacuum switch would be excessive vacuum errors reported by the AH400.  This would be reported as a vacuum error or chip lost error.

  - To adjust the SMAC vacuum switch go to the gantry screen and move the PNP head to an area that you can reach the vacuum switch.  Normally tape input or vision is good for this.

  - Next turn on the vacuum switch from the gantry screen.

  - On the vacuum switch you will see 2 adjustments.  1 is called HYS and is on the top and the other is called Set and is on the bottom.

  - Turn the top adjustment screw all the way anti-clockwise (left).

  - Next turn the set adjustment screw clockwise (right) until the light turns on.  Next turn the screw back to the left until the light just turns off.

  - Next block the hole on the vacuum cup with your finger

and see if the light comes on.  Then remove your finger and the light should turn off.  Try this 3 times and make sure that the light goes on and off properly.  If the does not turn off and on properly adjust the set screw a little until it works properly.

  - To adjust the option bay shuttle cup vacuum you will need to remove the access cover under the laser or labeler.

  - Directly under the shuttle are 2 vacuum generators and switches.

  - Go to the Shuttle/Options form the system screen.

  - Turn on the vacuum to shuttle 1 and 2.

4.12	Follow 4.4 to 4.7 for each switch.