#### DATA I/O Corporation

# 10525 Willows Road NE

Redmond, WA 98052

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

FAX: 425.867.6972

pmhelp@dataio.com

### Subject: Mitsubishi Servo Amp Jumper Installation

Model Affected: PP100

- PURPOSE:  To inform customers of a potential problem on some Mitsubishi servo amps.

2.0	TOOLS REQUIRED: Small Philips screwdriver

3.0	PARTS REQUIRED:  18 gage wire 4-6”

- INSTRUCTIONS:  Some PP100 systems with the Mitsubishi servo amps went out without a jumper installed.

  - Open the right side lower door of the PP100.  Locate the X and Y servo amps and see if you have the Yaskawa or the Mitsubishi servo amplifiers, see figures 1 and 2.

### Figure-1 YASKAWA Servo Amp		 Figure-2 MITSUBISHI Servo Amp

  - If you have Yaskawa you do NOT need to do anything.

  - If you have the Mitsubishi servo amplifiers, check the connector and see if you have the jumper installed.

  - If the jumper between P and D pins is missing, then:-

    - Shut down the PP100 and disconnect the main AC power input wire.

    - Remove the green connector, as shown in Figure-4

    - Install an 18-gauge wire between pin P and pin D, as shown in Figure-4

    - Re-connect the power cord and start-up the unit.

# Text boxes

Figure-4 Jumper Installed between P and D pins.

Figure-3 Jumper Not Installed