#### DATA I/O Corporation

# 10525 Willows Road NE

Redmond, WA 98052

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

FAX: 425.867.6972

FSE@dataio.com

### Subject: BGA FlashTOP Adapter Cleaning Procedure

### Subject: BGA FlashTOP Socket Removal and Replacement Procedure

Models Affected: PP100/PS200/PS300

- PURPOSES: To inform customers of the correct procedure for removing, cleaning and replacing sockets on BGA FlashTOP adapters.

- TOOLS REQUIRED:   3/16” Allen wrench, flat bladed screwdriver, and ¼” nut driver.

- PARTS REQUIRED: None

BGA FlashTOP Adapter Cleaning Procedure

| BGA FlashTOP Adapter Socket Removal Procedure |
| --- |
| CAUTION: | DO NOT PULL THE SOCKET FROM ABOVE AS THAT MAY CAUSE DAMAGE. |
| NOTE: | Remove sockets/interposer boards for these two reasons only: 1. To replace a damaged or worn socket/interposer board 2. To troubleshoot a socket problem by swapping sockets on an adapter board |

| BGA FlashTOP Adapter Socket Replacement Procedure |
| --- |
| CAUTION: | DO NOT PRESS UNTIL PINS ARE CORRECTLY LINED UP. IMPROPERLY ALIGNED PINS MAY CAUSE DAMAGE. |

# Text boxes

### Screw

Use the 3/32” hex wrench to loosen and remove the 4 screws that hold the metal cover to the adapter unit. The screws are held by 4 nylon standoffs on the bottom of the adapter unit.  Use the ¼” nut driver to hold the standoffs stationary while removing the screws.

### Standoff

When ready to clean, the adapter will look like this.

Use an ultrasonic cleaner with an alcohol and deionized water solution to clean the adapter.

Insert the flat bladed screwdriver between the socket/interposer board and the adapter board and gently loosen.

When socket/interposer board is loosened, gently remove from adapter board.

##### Socket Polarity Mark

Board Polarity Mark

Align the board and the socket by aligning the board polarity mark with the socket polarity mark.

Align the pins on the socket with the holes on the board. When pins are aligned, gently press down.

Reinstall the metal cover. Make sure to line up the standoffs between the metal cover and the main board.