#### DATA I/O Corporation

# 10525 Willows Road NE

Redmond, WA 98073

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

FAX: 425.867.6972

support@dataio.com

### Subject: P100 / PS-Series Laser PC and SMI Installation

This document describes how to Install the SMI (Serial Marking Interface) software on Handler Computer and Connect data cable between Laser and Handler Computer

After the above, PP100/PS_Series the marking file (e.g. mark001.mkh) will be loaded automatically on the LASER computer when the particular job, in which LASER marking is specified, on the AH400 opening screen.

# Requirements:

- AH400 V3.9 Service Release 9 (AH400 3.9.xx) or higher.

- NEWJOB.BAT 4/13/01, Batch file for creating new Job/Tasks – in DOS mode only

# “Serial Marking Interface” software (on 2 Disks)

This has to be installed on the LASER computer.

# Serial Cable (Data I/O PN:411-0011-001)

To be connected between the LASER computer and Handler Computer

Install new AH400 and Edit WINAH400.INI file

# Copy the AH400_39xx.ZIP on the handler computer’s hard disk and extract the file AH400_39xx.EXE	in directory C:\AH400_32\

# If Handler Computer’s “desktop” has AH400 icon, then edit the “shortcut” Target to point to the correct EXE file, namely: C:\AH400_32\AH400_39xx.exe

# On the handler computer’s desktop, update the AH400 Shortcut’s Target to reflect this new file: C:\AH400_32\AH400_39xx.exe

- In the directory C:\AH400_32\ edit the WINAH400.INI file and add this line:-

LaserRemoteConnection=TRUE

Cup2MarkPosMax=12000

Cup2MarkPosMin=10000

# Ensure that the LCD Touch Screen’s DB-9 is on the COM1 port of the Handler Computer.

B. Install NEWJOB.BAT file and create New Job

# Copy the NEWJOB.BAT file on the Server Computer (Novell Server), in the directory I:\MACHINE1\BATCH

##### Creating NEW Job/Task – in DOS Mode

# Select programming site which has the required adapter for the device

# On the related Programmer Computer (PC104), press ESCape from OPTIMA menu and Type N for New Job

# Type the New Job/Task’s name, example BIGJOB

# New Job Creation will prompt for:-

# "... Enter Adapter Name (ex: S273HREV1): "

# Type the adapter module name installed on the programmers. Typical adapter names are: -

# S273H – for TSOP-48 devices

# S286H – for TSOP-56 devices

# S717  –  for PLCC-32 devices

# Reference Vision file of the same name will be generated, example S273HREV1

# If laser marking is required, answer Y (yes) to the question:-

# Do you have 'Serial Marking Interface' Software on LASER PC (N/y)?

# At the next prompt “Drawing Filename:..” type the marking file name, without it’s extension mkh,  for example for mark001.mkh, type mark001

# Fill in other job related information and when finished type EXIT

# C. Install Interface Cable & Serial Marking Interface software.

- Install the  “null-modem” cable ((Data I/O PN:411-0011-001)) between Handler computer (COM2) and LASER computer (COM2).

- Install the Serial Marking Interface (SMI) software on the LASER computer.

- Insert Disk1 and double click on  SETUP.EXE. When asked for directory, select C:\Program Files\Serial Marking Interface\ directory.

- When SMI is installed, re-start the LASER computer.

- Start the Winmark Pro software.

- For all the mark files (*.mkh) change Mark Count to one (1):-

- Once mark files are created or changed, close the WinMark Pro software. For normal operation, the WinMark Pro software must be turned off and only the SMI software need be running on the LASER computer.

# Text boxes

Serial Cable on COM2

(PN:411-0011-001)

(DB9 connector)

Serial Cable on COM2

(DB9 connector)

Handler Computer

Laser Computer