#### DATA I/O Corporation

# 10525 Willows Road NE

Redmond, WA 98073

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

FAX: 425.867.6972

support@dataio.com

### Subject: PS300 / PP100 | Shuttle Transfer Belt Replacement Guide

This document provides guidelines on replacing the belt within the shuttle transfer assembly in the Option Bay attached with PP100 or PS300-series.

# Requirements:

# Shuttle Belt, Data I/O P/N 2640009001

# 6 feet for option bay with Tape-Out

# 5 feet for option bay with only Laser or Label marker

Loosen the four screws on the motor mount plate. See Figure 1. Slide the motor mount plate outboard to create slack in the shuttle belt.

Locate the shuttle. You may have to pull it out from inside the Programming Bay or from inside the optional Tape Output Module to access it.

Loosen the two screws holding the shuttle clamp to the shuttle. See Figure 2. Note how the belt ends attach to the clamp.

Remove the belt by gently pulling one end completely out of the machine. Keep the old belt for measuring the new belt length.

Using the old belt as a template, cut the new belt to the same length.

Route the belt through the system as shown in Figure 3.

Make sure all sprocket teeth mesh with the holes in the belt. See Figure 4.

- Connect the belt ends to the shuttle clamp as shown in Figure 5. Ensure that the teeth on the shuttle clamp are engaged with the holes on the belt. Re-attach the shuttle clamp to the shuttle.

- Slide the motor mount inboard. Use the measuring scale to set a 3/16 inch (0.475 cm) gap in the screw slot as shown in Figure 6.

If the belt is still slack, use the scissors to trim one tooth section from the belt end.

# Text boxes

Motor

Figure 3: Belt routing (top view)

Figure 6: Measure gap

Figure 5: Connect belt ends to shuttle clamp

Front of machine

Shuttle

Figure 4: Sprocket teeth mesh with belt

Figure 2: Loosen screws holding the shuttle clamp to the shuttle

Figure 1: Loosen four screws on motor mount plate