#### DATA I/O Corporation

# 10525 Willows Road NE

Redmond, WA 98052

Phone: 1.425.881.6444

Phone: 1.800.247.5700 (press 2)

FAX: 425.867.6972

pmhelp@dataio.com

### Subject: PP100 Programmer Software Update Procedure

Model Affected: PP100

- PURPOSE: To inform customer how to update the PP100 programmer software.

2.0	TOOLS REQUIRED: NONE

3.0	PARTS REQUIRED: CD or floppy disk.

- INSTRUCTIONS: If you have a CD with the PP100 software proceed to 5.0.  If you are going to download the software from the Data I/O Web page proceed to 4.1.

4.1	Go to the Data I/O web page. http://www.dataio.com

4.2	Go to Service/Technical Support.

4.3	Then select

4.4     Then select PP100.

4.5	On the download page select the released algorithm opt_dos.exe  (3 times per year A,B and C) or the Interim algorithms paldzipo.exe or prsdzipo.exe, released every Friday. Download the required file to your computer.

- Copy the files to a floppy disk and insert it in PP100’s Handler computer.

- From the handler computer, open Windows Explorer and go to directory I:\SPRINT.  Rename the file prom.exe to prom_old.exe  and pal.exe to pal_old.exe respectively. This will allow you to keep your old algorithms in case the interim release has any problems with your devices.

- Copy the paldzipo.exe or prsdzipo.exe to I:\Sprint and run the .exe files, which will extract prom.exe or pal.exe files. You will also have 2 files named lookup.txt and adapter.txt. Say yes to overwrite these files.  The lookup.txt and adapter.txt only apply to prsdzipo.exe.

- On the Server edit I:\MACHINE1\BATCH\START.BAT file and if not already present, add these two lines:-

COPY I:\SPRINT\ADAPTER.TXT D:\

COPY I:\SPRINT\LOOKUP.TXT D:\

- Next go to the rear of the PP100 and turn off the circuit breaker to the programmers. Then turn the circuit back on. This will copy the new files from the network computer to the programmers.

- Now you can just run your job normally.