Modification for TOP48

Dear SPRINT user,

When you receive the screen message "Please ask your distributor for MODxxx..., a hardware change is nrequired for the device you are attempting to program. A qualified Surface Mount Technician must do the required MOD(s).  If you do not have one available, you should contact the nearest Data I/O approved Service Center.  Please note that this is a billable service.

This modification concerns devices that require fast pull-ups on a special pins or that have the supply-pins at non-standard locations. Look to the schematic on the page 2 of this document to locate the positions of the pins and the requested solder pads.

1)	Remove the TOP48DIP of your programmer.

2.)	Connect the requested solder pad to the requested pin by an isolated wire

Note :	The solder pads are splitt into two different parts, one circle and one square - please

use always the square part to connect the isolated wire with the requested pin.

3.)	Connect the TOP to the programmer and reselect the device

The message "Please ask your distributor...." should no longer appears on the screen.

| MOD | Device | Signal | Pin-number |
| --- | --- | --- | --- |
|  | 15/94 | MC68HC711D3 | GND : JP5 | 5 |
| 16/94 | Z86E02/04/07/08 | VCC : JP7 | 20 |
| 20/94 | MC68HC11A1/A8 | GND : JP5 | 23 |
| 21/94 | SDA 2506 | VCC : JP7 | 23 |
| 13/95 | Cypress PALCE16V8 |

S7

S8

19

| 20 |
| --- |
| 20/95 | AMD Am27S27 | VCC : JP7 | 35 |
| 1/96 | SGS M92256 | GND : JP5 | 23 |
| 5/96 |

Philips

ABT22V10A

LVT22V10

solder a 10K( resistor

between JP7 and pin 33 and

| between JP8 and pin 34 |
| --- |
| 12/96 | COP87L22/42 | VCC : JP7 | 20 |
| 13/96 |

COP87L20/40/84

| COP8SAx7-28p | VCC : JP7 | 16 |
| --- | --- | --- |
| 14/96 | COP87L88 | GND : JP5 | 37 |
| 19/96 | PZx032 | GND : JP5 | 32 |
| 20/96 | MC68HC705J1A | VCC : JP7 | 23 |
| 4/97 | PZx064 | GND : JP5 | 44 |

| MOD | Device | Signal | Pin-number |
| --- | --- | --- | --- |

13/97

not with new ASICs

Atmel

| ATF1500/A | S7 or S8 | 6 |
| --- | --- | --- |
| 14/97 | COP SAx7-16 |

VCC : JP7

GND : JP5

22

| 27 |
| --- |
| 16/97 | Xicor 88C75 | VCC :JP7 | 48 |
| 22/97 | Intel 87C42 (DIL) | CLOCK : JP2 | 7 |
| 18/98 | MC68HC805PV8 | CLOCK : JP2 | 30 |
| 19/98 | Motorola 68HC705CJ4 | JP1 or JP2 or JP3 or JP4 | 43 |
| 2/99 | Samsung KM29N040T |

VCC : JP7

GND : JP5

44

5

4/99

Atmel

AT45dxxSOIC

| 28pin | GND : JP5 | 11 |
| --- | --- | --- |
| 5/99 |

Atmel

AT45dxxTSOP

28 pin

VCC : JP7

GND : JP5

16

17

6/99

Mitsubishi

M37510EFFP

| 176 pin | VCC : JP7 | 39 |
| --- | --- | --- |
| 7/99 | Xilinx 1704LVC |

GND : JP5

GND : JP6

4

| 22 |
| --- |
| 8/99 | AT45DB081/D081-TSOP(32pin) |

VCC : JP7

| GND : JP5 | 39 40 |
| --- | --- |
| 9/99 | M29W102BB –TSOP(40 pin) |

VCC : JP7

| GND : JP5 | 24 42 |
| --- | --- |
| 10/99 | AS29F080 –SO(44 pin) |

VCC : JP7

| GND : JP5 | 3 11 |
| --- | --- |
| 12/99 | TI MSP430P112 | VCC: JP7 | 16 |
| 13/99 | ST72T101xx |

GND: JP5

CLK: JP2

37

12