ECN 3/93

Dear SPRINT user,

For programming the DALLAS1245, AMD29F010, AMD29F040 and some additional devices, a hardware change is necessary. A qualified Surface Mount Technician must do the required MOD(s).  If you do not have one available, you should contact the nearest Data I/O approved Service Center.  Please note that this is a billable service.

Remove the TOP432 of your programmer.

Remove the four screws holding the PCB in the TOP and take out the PCB. Turn it to its component side and look for the area shown in Figure 1.

Solder a 1k( resistor between pin 25 of the programming socket 1 and pin 1 of the resistor-network. This pin is next to pin 32 of the programming socket.  Refer to Figure 1.

Solder a second 1k( resistor between pin 29 of the programming socket 1 and pin 1 of the resistor-network. To do this we recommend you solder it to the wire of the first resistor.

Solder a third 1k( resistor between pin 31 of the programming socket 1 and pin 1 of the resistor-network. To do this we also recommend you solder it to the wire of the first resistor.

Turn the PCB to its solder side and look for the area shown in Figure 2.

Solder a 10k( resistor between pin 25 and 28 of the VG-connector. Refer to Figure 2.

Reassemble all parts of TOP432.  Be careful not to tighten the screws too hard.

Attach the TOP432 to your programmer again.

Figure 1

Component side of TOP432

(Upper right corner)

Figure 2

Solder side of TOP432

(Lower right corner)